## Slide 1: Algoritmo genético para planejamento de caminhos baseados em curvas de Bezier
Trabalho Final de Robótica Móvel - 2018/2
Departamento de Ciência da Computação
Universidade Federal de Minas Gerais
Belo Horizonte – MG – Brasil
Thiago Meireles Grabe

## Slide 2: Introdução
Planejamento de Trajetórias
  Encontrar um conjunto de configurações VÁLIDAS para que o robô navegue de um ponto inicial a um ponto final.
Motivação
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 3: Introdução
Motivação
Planejamento de Trajetórias
  Encontrar um conjunto de configurações VÁLIDAS para que o robô navegue de um ponto inicial a um ponto final de forma eficiente!!!
    Tempo de deliberação;
    Contorno eficiente de obstáculos;
    Caminho “suave”.
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 4: Introdução
Trabalhos Relacionados
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 5: Introdução
Formulação do Problema
Dado um mapa e suas características (obstáculos), uma configuração inicial e final, qual caminho o robô deve seguir para ir de um ponto a outro de forma eficiente, sem mudanças bruscas de direção e sem colisão com obstáculos? É possível utilizar um algoritmo genético para planejar um caminho?
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 6: Metodologia
Curvas de Bezier
Curvas de Bezier são curvas paramétricas polinomiais no plano ou no espaço.
Utilizadas em modelagem tridimensional, animações, engenharia e arquitetura.
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 7: Metodologia
Algoritmo Genético
Algoritmo evolucionário de otimização e busca para diversos problemas.
São eficientes para busca de soluções ótimas ou quase ótimas.
Figura da disciplina Computação Natural – Gisele L. Pappa
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 8: Metodologia
Planejamento de trajetória
Como premissa principal, o mapa é conhecido bem como a posição do agente.
Os pontos inicial e final são, o primeiro e último ponto de controle, da curva de Bezier.
Os demais z pontos de controle são escolhidos aleatoriamente.
Curva de Bezier é definida e os n pontos que definem a curva são armazenados em um vetor (solução candidata).
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 9: Metodologia
Planejamento de trajetória
Todas as soluções são avaliadas de acordo com uma fitness específica do trabalho.
  ϒ Fitness a ser calculada
  Curvatura da trajetória normalizada
  Distância euclidiana da trajetória normalizada
  Φ Obstáculos na trajetória
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 10: Metodologia
Planejamento de trajetória
Operadores genéticos elitistas são chamados dada uma devida probabilidade de ocorrência:
  Mutação = 10%
  Cruzamento = 90%
    Mutação permite busca por todo o espaço de busca.
    Cruzamento permite a convergência para um mínimo (local ou global).
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 11: Experimentos
Planejamento de Trajetórias
  Parâmetros:
    Número de Indivíduos
    Número de Gerações
    Quantidade de pontos de controle da curva de Bezier
    Quantidade de configurações por trajetória
    Probabilidade de mutação e cruzamento
    Fitness mínima (elitismo)
    Obstáculos
Número de Gerações
150
300
350
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 12: Resultados
Planejamento de Trajetórias
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 13: Resultados
Planejamento de Trajetórias
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 14: Conclusões
Trabalho Final – Robótica Móvel
Paradigma robótico hierárquico
Algoritmo genético utilizando cruzamento e mutação como operadores genéticos apresentou soluções válidas
Planejamento de caminho é feito pelo método proposto
Elitismo causa problemas de mínimos locais
Ajuste de parâmetros de forma empírica (esperado)
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 15: Conclusões
Trabalhos Futuros
Controlar elitismo para explorar melhor espaço de busca
Aprimorar a função de fitness
Ajuste de parâmetros para diversos mapas ou conjunto de mapas
Melhorar tempo de deliberação
Implementação para robôs diferenciais
Notes: Path planning and trajectory tracking are two of the fundamental tasks when it comes to mobile robots
Can be studied as a two-step approach. First, plan a path from a start position to a goal position (path planning). Second, then track the created path (trajectory Tracking).
On image: robot represented as a ball. Red ball is robot’s initial position, green ball is the desired destination. Triangles are the planned path, green line (full and dashed) the tracked trajectory based on the triangle path.

## Slide 16
Obrigado!
Thiago Meireles Grabe
thiago.grabe@dcc.ufmg.br